## Slide 1
WEEK 2
LOOPS & SERIAL PORT
through the PIR Motion Sensor
Data Science with ESP32 & Python | Grade 8
▸ While Loops
▸ For Loops
▸ Serial Port
▸ String Methods
▸ Try / Except
▸ Auto Port Detection
Read sensor data forever. Loop, listen, label, repeat.

## Slide 2
WEEK 1 RECAP + WHAT WE BUILD TODAY
Last week: Python basics. This week: use them to read LIVE motion sensor data in a continuous loop!
Completed — Week 1
✅ Variables lux = 48.5
✅ Data types int, float, str, bool
✅ Print print(f"{lux} lx")
✅ If / else Bright / Medium / Dark
✅ Imports import serial
✅ Comparisons lux > 80
New — Week 2
🆕 while True loop forever
🆕 for loop loop a set number of times
🆕 ser.readline() read from ESP32
🆕 line.split() extract the value
🆕 line.strip() clean up whitespace
🆕 try/except handle errors safely
What we build today — Live PIR Motion Console
Looking for ESP32... Found ESP32 on COM5 Reading PIR data... Press Ctrl+C to stop
Time Score Status
18:25:10 45 Motion Detected
18:25:11 0 No Motion
Everything in Week 2 ADDS to Week 1. You already know variables and if/else — now we loop forever!

## Slide 3
CONCEPT 1 — WHILE LOOPS
A while loop keeps running AS LONG AS a condition is True. while True means run forever — never stop!
The Security Guard Analogy
A security guard does NOT check the door once then go home. They check continuously — all day in a loop.
Your while True loop IS the security guard. It reads the sensor, prints the result, then immediately loops back to check again.
Why we need while True for sensors:
Without a loop, Python reads ONE line then STOPS. But the sensor keeps sending data every 100ms! We need while True to keep reading forever — until you press Ctrl+C.
While Loop — 3 forms you need to know
# Form 1: Loop forever (most common)
while True:
print("Still running!")
# Form 2: Loop while condition is True
count = 0
while count < 10:
count = count + 1
# Form 3: Stop with break
while True:
if score > 100:
break # exit the loop
INDENTATION RULE:
All code INSIDE the while loop must be indented 4 spaces. Without indentation Python gives an IndentationError!
To stop a while True loop: press Ctrl+C in the terminal. Python will stop immediately and cleanly.

## Slide 4
CONCEPT 2 — FOR LOOPS
A for loop runs a FIXED number of times. Perfect for scanning a list — like all COM ports to find ESP32!
While vs For — when to use each
while True
Read sensor forever — no end
while x < 10
Loop until condition is False
for item in list
Loop through every item in list
for i in range(5)
Loop exactly 5 times
For loop in our PIR sensor code:
We use a for loop to scan ALL connected COM ports and find the ESP32. The loop checks every port one by one until it finds the CH340 USB chip name.
For loops with our sensor
# Find ESP32 — loop through all ports
PORT = None
for port in list_ports.comports():
if "CH340" in port.description:
PORT = port.device
# Loop through a list of readings
readings = [45, 0, 72, 0, 88]
for score in readings:
if score > 0:
print("Motion:", score)
# Loop exactly 10 times
for i in range(10):
print("Reading number:", i+1)
KEY DIFFERENCE:
while True runs FOREVER until stopped. for loop runs a FIXED number of times then stops automatically.
In our sensor code: for loop finds the port ONCE, then while True reads data FOREVER. Both work together!

## Slide 5
CONCEPT 3 — SERIAL PORT & readline()
The serial port is the USB connection between Python and ESP32. readline() picks up one line at a time.
The Radio Analogy
serial.Serial(PORT, 9600) is like tuning your radio to a specific station.
PORT = "COM5" is the station.
9600 = baud rate = speed of data.
readline() = waiting to hear the next sentence from ESP32.
What is Baud Rate (9600)?
Both Arduino and Python must use the SAME baud rate or nothing works.
Arduino: Serial.begin(9600)
Python: serial.Serial(PORT, 9600)
They must match exactly. 9600 = 9600!
Serial port in Python — step by step
import serial
import serial.tools.list_ports
# Step 1: Find the port automatically
PORT = None
for port in list_ports.comports():
if "CH340" in port.description:
PORT = port.device
# Step 2: Open the connection
ser = serial.Serial(PORT, 9600, timeout=1)
# Step 3: Read one line at a time
while True:
line = ser.readline()
# line is raw bytes — decode next!
readline() returns BYTES not text!
You must decode it: line = ser.readline().decode("utf-8", errors="ignore").strip()
RULE: Close Arduino IDE Serial Monitor BEFORE running Python — only ONE program can use COM5 at a time!

## Slide 6
CONCEPT 4 — STRING METHODS
String methods extract, clean and transform text. Essential for reading sensor data from the serial port.
Decode
.decode("utf-8", errors="ignore")
Convert bytes to readable text
raw = ser.readline()
line = raw.decode("utf-8", errors="ignore")
Strip
.strip()
Remove whitespace and newlines at ends
line = " 48.5\n "
line = line.strip() # becomes "48.5"
Split
.split(":")
Cut text at a character into a list
line = "Motion: 45"
parts = line.split(":") # ["Motion"," 45"]
In
"text" in line
Check if text exists inside string
if "Motion" in line:
# only runs on motion lines
Chain them all: line = ser.readline().decode("utf-8", errors="ignore").strip() — one clean line!

## Slide 7
CONCEPT 5 — TRY / EXCEPT
Real sensor data is messy. try/except catches errors so your program keeps running instead of crashing!
The Problem — Without try/except
line = "" # empty line from ESP32
value = int(line) # CRASH!
# ValueError: invalid literal for int()
The Solution — With try/except
try:
value = int(line) # attempt this
except:
pass # skip bad lines silently
Try/Except — all the forms
# Basic — catch any error
try:
value = int(line)
except:
pass
# Specific — catch exact error type
try:
value = float(line.split(":")[1])
except ValueError:
print("Bad line — skipping")
# With else — runs only if no error
try:
value = int(line)
except: pass
else: print("Success:", value)
When to use try/except:
Converting text to number | Reading files | Connecting to hardware | Any real-world data operation
pass means do nothing and move on. It is the polite way to skip a bad reading without crashing the whole program!

## Slide 8
PUTTING IT ALL TOGETHER — THE PIR MOTION SCRIPT
Every concept from Week 1 AND Week 2 is in this real script. Every line has a job.
import serial
import serial.tools.list_ports
from datetime import datetime
BAUD = 9600
PORT = None
for port in list_ports.comports():
if "CH340" in port.description:
PORT = port.device
ser = serial.Serial(PORT, BAUD, timeout=1)
while True:
line = ser.readline().decode(
"utf-8", errors="ignore").strip()
if line:
try:
score = int(line)
now = datetime.now().strftime("%H:%M:%S")
if score > 0:
status = "Motion Detected"
else:
status = "No Motion"
print(f"{now} {score:<10} {status}")
except:
pass
IMPORTS — Week 1: load all libraries at top
VARIABLE — Week 1: store baud rate value
FOR LOOP — Week 2: scan every USB port
SERIAL — Week 2: open COM5 connection
WHILE TRUE — Week 2: read sensor forever
STRING METHODS — Week 2: decode + strip
TRY/EXCEPT — Week 2: handle bad lines
IF/ELSE — Week 1: classify motion status
F-STRING PRINT — Week 1: show result
PASS — Week 2: skip errors silently
This script combines ALL of Week 1 + Week 2. Every concept has a job. Nothing is wasted!

## Slide 9
WEEK 2 COMMON ERRORS & FIXES
These are the new errors you will see this week. Read the message carefully — Python always tells you what went wrong!
UnicodeDecodeError
"utf-8 codec can't decode byte 0x9e"
Cause: ESP32 sends garbage bytes on first connect
Fix: Add errors="ignore" to decode()
line.decode("utf-8", errors="ignore")
TypeError: int() argument
"must be a string, not NoneType"
Cause: readline() returned nothing — line is empty
Fix: Check if line is not empty first
if line:
score = int(line)
AttributeError: NoneType
"NoneType has no attribute 'device'"
Cause: ESP32 not found — PORT is still None
Fix: Check PORT is not None before using it
if PORT:
ser = serial.Serial(PORT, 9600)
ValueError: invalid literal
"invalid literal for int(): 'Initializing...'"
Cause: Trying to convert a word to a number
Fix: Use try/except to skip non-number lines
try:
score = int(line)
except: pass
Most Week 2 errors come from empty lines or startup messages. Always use try/except and check if line: first!

## Slide 10
WEEK 2 — PRACTICE EXERCISES
Try these exercises in VS Code with the PIR sensor connected. Do them in order!
01
Run the simple PIR script
Beginner
1. Upload PIR Arduino code to ESP32 first
2. Close Arduino IDE completely
3. Run simple_pir.py in VS Code terminal
4. Wave your hand in front of the sensor
Goal: See Time | Score | Status printing in your terminal
02
Add a loop counter
Intermediate
1. Add count = 0 before the while True loop
2. Inside the loop add: count = count + 1
3. Change print to include count in output
4. Watch the counter increase with every reading
Goal: Each line shows Reading #1, #2, #3 with motion data
03
Count total motion events
Intermediate
1. Add motion_count = 0 before the loop
2. Every time score > 0 do: motion_count += 1
3. Include motion_count in your print statement
4. Think: what does this number tell you about the room?
Goal: Track and display total motion events detected so far
04
Find your own COM port
Advanced
1. Write a new script from scratch
2. Use for port in list_ports.comports()
3. Print port.device and port.description for each
4. Identify the ESP32 from the CH340 description
Goal: Understand exactly how Python auto-detects COM5
Challenge: Save motion events to a CSV file with timestamp and score — combine Week 1 and Week 2 skills!

## Slide 11
WEEK 2 COMPLETE!
Everything you learned this week through the PIR Motion Sensor:
🔄 While loops
while True: read()
Completed
🔁 For loops
for port in ports:
Completed
📡 Serial port
serial.Serial(PORT,9600)
Completed
✂️ String methods
.decode().strip().split()
Completed
🛡️ Try / Except
try: ... except: pass
Completed
🔍 Auto port detect
"CH340" in description
Completed
NEXT — Week 3: Lists, Functions & CSV through the DHT11 Temperature Sensor
You will store readings in a list, write reusable functions and save data to CSV for Excel analysis!